The TwinCAT3 code that has been developed has been done in a way which allows it to easily work with the SOEM library as well. This means a few small adapter funcionalities have been added so that both SOEM and TwinCAT3 can work with the same source files.

The 'toplevel' TwinCAT3 code is in Module1.cpp. This file essentially performs the same functionality as soem_main.cpp for soem.

The SOEM implementation uses seperate structures to access data on slave devices. For the wago stepper motors there is an array of struct wago_stepper_t. This array represents a single input or output area for the steppers motors (the input and output areas share the same layout).
In code there is a 3x2 array which represents the 3 wago stepper devices input and output layouts. Currently index 0 represents output and index 1 represents input (1 looks like i, 0 looks like o :D). There is a #define of WAGO_OUTPUT_SPACE and WAGO_INPUT_SPACE which are 0 and 1 respectively.

These structures are actually pointers to the io spaces. Each element needs to receive the correct memory address for access to the respective device io space. This means the m_Inputs data area needs to be connected to the struct wago_steppers_t array correctly. This is why the SetObjState PS method contains the following.
At the time of writing, the other devices have not yet been set up in the TwinCAT3 software. They will need to be connected similarly.
HRESULT CModule1::SetObjStatePS(PTComInitDataHdr pInitData)
{
m_Trace.Log(tlVerbose, FENTERA);
HRESULT hr = S_OK;
IMPLEMENT_ITCOMOBJECT_EVALUATE_INITDATA(pInitData);

// TODO: Add initialization code

wago_steppers[0][WAGO_INPUT_SPACE] = (struct wago_stepper_t*) &(m_Inputs.wago_stepper_inputs0);
wago_steppers[1][WAGO_INPUT_SPACE] = (struct wago_stepper_t*) &(m_Inputs.wago_stepper_inputs1);
wago_steppers[2][WAGO_INPUT_SPACE] = (struct wago_stepper_t*) &(m_Inputs.wago_stepper_inputs2);

wago_steppers[0][WAGO_OUTPUT_SPACE] = (struct wago_stepper_t*) &(m_Outputs.wago_stepper_outputs0);
wago_steppers[1][WAGO_OUTPUT_SPACE] = (struct wago_stepper_t*) &(m_Outputs.wago_stepper_outputs1);
wago_steppers[2][WAGO_OUTPUT_SPACE] = (struct wago_stepper_t*) &(m_Outputs.wago_stepper_outputs2);

m_Trace.Log(tlVerbose, FLEAVEA "hr=0x%08x", hr);
return hr;
}

The cyclic function currently displays a message in the TwinCAT3 ErrorList window when the sick laser state changes. It also calls the state_machine function which updates the state of i/o's and the state machine controlling the wago stepper motors.

HRESULT CModule1::CycleUpdate(ITcTask* ipTask, ITcUnknown* ipCaller, ULONG_PTR context)
{
HRESULT hr = S_OK;
static uint8_t current_sick;
static uint8_t last_sick = 0;

/* notify about changes to state of sick sensors */
current_sick = m_Inputs.EK1002_BITS;

if (current_sick != last_sick)
printf("sick: changed to %x from %x\n", current_sick, last_sick);
last_sick = current_sick;

state_machine();

return hr;
}

A printf function needs to be created so that debug messages can be done the same way on both SOEM and TwinCAT3. This has been added to the main module class as m_Trace is by default only available from the class.
To make this function work correctly the m_Trace.LogV method needs to exist (The existing m_Trace.Log is not suitable for calling through another function).
void printf(const char *fmt, ...)
{
va_list args;
va_start(args, fmt);

m_Trace.LogV((PCHAR) fmt, args);

va_end(args);
}
m_Trace is an instance of Cctrace. Cctrace is defined in TcInterfaces.h. I'm not sure where this file is, you can get to it in visual studio by right clicking any m_Trace.Log call and clicking goto declaration. Then right click on Cctrace and click open declaration. The following method needs to be added:
void LogV(PCHAR szFormat, va_list pArgs)
{
if (m_spSrv != NULL)
{
DWORD msgCtrlMask = ADSLOG_MSGTYPE_STRING;

m_spSrv->TcReportLogV( msgCtrlMask, szFormat, pArgs );
}
}