# Intro
The SOEM implementation uses the SOEM library available here: http://soem.berlios.de/
When using the SOEM implementation it is absolutely required to lock and unlock access to the SOEM library (and the IOmap), if you fail to do this in any situation the program may work intermittently or not at all. As always, try to keep the locks used for as few instructions as possible so as to increase performance and reduce timing delays.
# Basic Layout
The implementation running SOEM uses 3 threads. The two work threads are the main thread and the EtherCAT thread. The third thread is used to handle commandline input (stops the main program from blocking when handling input).
# Source and Header File dependencies
The SOEM implementation depends on an number of source and header files.
## Shared with TwinCAT3 implementation
As a number of files are shared with the TwinCAT3 implementation the files can be found in the TwinCAT3 project. The file structure will need to be restructured to make the distinction between files clear. I haven't yet got around to this, hopefully this will be done before I finish.
### Headers
error.h, state_machine.h, wago_steppers.h
### Sources
state_machine.c, wago_steppers.c
## SOEM only
### Sources
soem_main.c
### Other
Makefile

# Main Thread
The main thread starts by processing commandline options. This is done using POSIX getopt, details of how getopt works can be found here: http://linux.die.net/man/3/getopt

Following this the priority of this thread is increased. Details of this can be found here: http://man7.org/linux/man-pages/man2/sched_setscheduler.2.html
The thread is scheduled using FIFO scheduling policy. This means if the thread is preempted execution returns to the thread as soon as the preempting thread is dealt with (the thread is not rescheduled).

It may be possible to further increase the EtherCAT performance by calling sched_yield(). However this sort of optimization should be avoided for as long as possible as it can have a negative affect on performance when the program is modified.

The main thread then sets up the input handling thread (discussed in Commandline input thread).

The main thread then sets up the EtherCAT thread (discussed in EtherCAT thread).

Finally the main thread enters the 'main loop' which cyclically executes the state machine.
# EtherCAT thread
The EtherCAT thread was created so that the logic for the state machine could be made simpler and could be separated from SOEM specific EtherCAT code. This thread calls the ec_send_processdata() and ec_receive_processdata() functions which update the master and slave I/O data. By placing this in a second thread it makes timing of these updates more reliable (if the update calls are made from the thread executing the state machine, the state machine would block the I/O syncing functionality making update timings unreliable).
# Commandline input thread
This thread was made to handle commandline input. It could be used at a later time to control the EtherCAT devices using the keyboard. Right now it is only used to signal to the main program that we would like to quit.
# Building
The makefile has support for building a standard executable (make all), a debug executable (make debug), and cleaning up the build file (make clean). The makefile may need to be modified to compile correctly if your setup is different. Most likely only the BASEDIR variable will need to be changed.